## Slide 1: Exploiting Dense Sensitivity Matrices in Linear Optimal Power Flow
Brent Eldridge, Johns Hopkins University
Anya Castillo, NextEra Analytics
Ben Knueven, National Renewable Energy Laboratory
Manuel Garcia, Sandia National Laboratories

## Slide 2: Outline
Background
Why are dense constraints better for large-scale DCOPF?
Modeling simplifications
Preliminary results
Linear OPF formulations
Funding from U.S. Department of Energy’s Office of Electricity through the Advanced Grid Modeling program under project title ``Reassessing the Market—Computation Interface to Enhance Grid Security and Efficiency.''

## Slide 3: Optimal Power Flow underlies many market applications
OPF
Unit commitment
Contingency analysis
Real time dispatch
Transmission switching

## Slide 4: Comparison of AC and DC approaches
AC OPF-based models
Physics is correct
Nonlinear, nonconvex
Uses real and reactive power
Relaxation (SDR,SOCR,QCR) to convex program
  Promising approach, but…
  Poor scaling in large systems
  Nonlinear
  Unsuitable for many applications
DC OPF-based models
Physics is approximated
Linear, convex
Only considers real power
B-theta and distribution factor (PTDF) formulations
  B-theta common in academic literature
  PTDF used in ISO applications

## Slide 5: Optimal power flow is not solved in isolation
Consider the “outer loop”
PTDF advantages:
  Linear
  Compact formulation
  Nonbinding constraints can be dropped
AC OPF and B-theta require the full explicit formulations
  Huge model size for AC OPF and AC OPF relaxations (SDP, etc.)
Determine important constraints
Calculate sensitivities
Solve OPF
Are all constraints satisfied?
Solve DC power flow on full network

## Slide 6: Research Questions for Linear OPF
How accurate can linear OPF models be?
What is the computational “cost” of more accurate OPF approximations?
What kind of simplifications can improve computational performance of dense OPF formulations?
What is the impact on solution accuracy?

## Slide 7: Dense Optimal Power Flow: Distribution factor (PTDF) derivation
Standard DC power flow assumptions result in:
Substitution into linear power balance constraints:
Define the PTDF as:
Issue: the B-theta power flow constraint matrix is sparse, so inverting and calculating results in a dense constraint matrix.
Notation:
Power flow:
Power demand:
Power generation:
Voltage angle:
Adjacency matrix:
Susceptance mat.:

## Slide 8: Four proposed models: Getting more accuracy out of linear OPF
Sparse (S-LOPF)
  First-order Taylor series approximation of decoupled AC power flow
  Mid-line power flow (Garcia et al., 2019)
Dense (D-LOPF)
  Dense factorization of the S-LOPF
Condensed (C-LOPF)
  Summation of branch losses to a system-wide loss variable
  Loss distribution factors to approximate effect of losses on branch flows
Real power (P-LOPF)
  Assume fixed voltages and reactive power flow
  Basically AC-linearized DC OPF
MORE APPROXIMATE

## Slide 9: Sparse Linear OPF model (S-LOPF)
Cost minimization
Linear balance constraints
First-order Taylor series expansion of power flow and branch losses
  and offsets are calculated from the AC power flow equations
  Analogous to
Transmission constraints
  Piece-wise linear apparent power limits
  Upper/lower voltage magnitude limits
Generator constraints

## Slide 10: Dense Linear OPF model (D-LOPF)
Cost minimization
System real power balance
  Reactive balance is unnecessary
Redefine , and using PTDF-like distribution factors
Other constraints stay the same

## Slide 11: Condensed Linear OPF model (C-LOPF)
Cost minimization
System power balance with system power losses
Reduce number of constraints by summing and constraints
Approximate branch losses with loss distribution factor in constraints
Generator constraints stay the same

## Slide 12: Real Power Linear OPF model (P-LOPF)
Cost minimization
System power balance with system power losses
Remove reactive power and voltage magnitude constraints
Fix reactive power and voltage variables in constraints
Generator constraints stay the same

## Slide 13: Methodology
Calculate Sensitivities
Real/Reactive power flow and line losses
Solve LOPF
Solved using Gurobi
Solve
AC OPF
Solved using IPOPT
Solve AC Power Flow
Calculate power flow errors and violations
Basepoint solution
Voltage magnitude
S/D/C/P-LOPF
Sparse and dense calculations
B-theta/PTDF
Simulates “actual” dispatch from OPF solution
Change Demand
Uniform multiplier from 0.9 to 1.1
0.01 increments
Extensive set of test cases:
PRELIMINARY results use full methodology to case588_sdet, nominal demand only to case6515_rte
'pglib_opf_case3_lmbd’,
'pglib_opf_case5_pjm’,
'pglib_opf_case14_ieee’,
'pglib_opf_case24_ieee_rts', 'pglib_opf_case30_as' 'pglib_opf_case30_fsr', 'pglib_opf_case30_ieee', 'pglib_opf_case39_epri', 'pglib_opf_case57_ieee', 'pglib_opf_case73_ieee_rts', 'pglib_opf_case89_pegase', 'pglib_opf_case118_ieee', 'pglib_opf_case162_ieee_dtc', 'pglib_opf_case179_goc', 'pglib_opf_case200_tamu', 'pglib_opf_case240_pserc', 'pglib_opf_case300_ieee', 'pglib_opf_case500_tamu', 'pglib_opf_case588_sdet', 'pglib_opf_case1354_pegase', 'pglib_opf_case1888_rte', 'pglib_opf_case1951_rte', 'pglib_opf_case2000_tamu', 'pglib_opf_case2316_sdet', 'pglib_opf_case2383wp_k', 'pglib_opf_case2736sp_k', 'pglib_opf_case2737sop_k', 'pglib_opf_case2746wop_k', 'pglib_opf_case2746wp_k', 'pglib_opf_case2848_rte', 'pglib_opf_case2853_sdet', 'pglib_opf_case2868_rte', 'pglib_opf_case2869_pegase', 'pglib_opf_case3012wp_k', 'pglib_opf_case3120sp_k', 'pglib_opf_case3375wp_k', 'pglib_opf_case4661_sdet', 'pglib_opf_case6468_rte', 'pglib_opf_case6470_rte', 'pglib_opf_case6495_rte', 'pglib_opf_case6515_rte', 'pglib_opf_case9241_pegase', 'pglib_opf_case10000_tamu', 'pglib_opf_case13659_pegase'

## Slide 14: “Vanilla” Implementations: DC OPF / LOPF / AC OPF
Solution Speed - cases with 3-588 buses
AC Power Flow Error - case2383wp_k
Error accumulation
Solution speed
Accuracy
PRELIMINARY RESULTS

## Slide 15: Methodology – “Lazy” Constraint Algorithm
The lazy constraint algorithm can be implemented on “dense” OPFs
  Implemented with Gurobi’s persistent solver
  D/C/P-LOPF and PTDF formulation of the DC OPF
  Reduces transmission constraints to around 5% of full model
  Reduces overall model size to about 50%
Not possible on sparse (S-LOPF/B-theta) formulations
  Removing line results in a new topology
Calculate Sensitivities
Solve LOPF
Solve
AC OPF
Solve AC Power Flow
Change Demand
Select Monitored Constraints
Check Violations

## Slide 16: Lazy algorithm benefits cases with >100 buses
Cases with 3-89 buses
Cases with 118-588 buses
The lazy algorithm only provides improvement on larger cases
PRELIMINARY RESULTS

## Slide 17: Hybrid line loss constraints for D-LOPF
Lazy algorithm does NOT allow us to ignore branch loss constraints
Solution: implement a hybrid model with residual losses
Result is similar to C-LOPF formulation
(case3375wp_k)
PRELIMINARY RESULTS

## Slide 18: Loss summation in C-LOPF and hybrid D-LOPF can cause accumulation of power flow errors
Hybrid/C-LOPF error accumulation (case4661_sdet)
C-LOPF error accumulation (case6495_rte)
PRELIMINARY RESULTS

## Slide 19: Factor truncation improves constraint sparsity but can also accumulate power flow errors
Dense models can be made more “sparse” by eliminating small coefficients
Errors are usually small
PRELIMINARY RESULTS

## Slide 20: Factor truncation improves constraint sparsity but can also accumulate power flow errors
Dense models can be made more “sparse” by eliminating small coefficients
Errors are usually small
Distortions in case3375wp_k
PRELIMINARY RESULTS

## Slide 21: Conclusions

## Slide 22: How accurate can LOPF results be?
Normalized total cost with nominal demand (up to case6515_rte)
Chart: 
| full | full | e2 | e2 | e2 | e2 | full | acopf | slopf | dlopf | clopf | plopf | ptdf | btheta
case
case3_lmbd | 1 | 0.99028 | 0.99028 | 0.99017 | 0.99875 | 0.97991 | 0.97955
case5_pjm | 1 | 0.99999 | 0.99999 | 0.99999 | 0.99736 | 0.9959 | 0.9959
case14_ieee | 1 | 1 | 0.99995 | 1 | 1 | 0.9419 | 0.9419
case24_ieee_rts | 1 | 1 | 1 | 1 | 1 | 0.96289 | 0.96289
case30_as | 1 | 1 | 1.0001 | 1 | 1 | 0.95577 | 0.95577
case30_fsr | 1 | 0.99936 | 0.99933 | 0.99936 | 0.9999 | 0.98165 | 0.98165
case30_ieee | 1 | 0.99999 | 1 | 0.99999 | 0.99234 | 0.91014 | 0.91423
case39_epri | 1 | 0.99809 | 0.99809 | 0.99809 | 0.99993 | 0.98897 | 0.98844
case57_ieee | 1 | 0.99883 | 0.99853 | 0.99883 | 0.99883 | 0.92507 | 0.92507
case73_ieee_rts | 1 | 1 | 0.99994 | 1 | 1 | 0.96437 | 0.96437
case89_pegase | 1 | 0.99887 | 0.99948 | 0.99941 | 9999 | 0.97726 | 0.97813
*Infeasible
A few cases with >1% gap
PRELIMINARY RESULTS

## Slide 23: What is the computational “cost”?
Normalized solution time at nominal demand (up to case6515_rte)
Chart: 
| full | full | e2 | e2 | e2 | e2 | full | acopf | slopf | dlopf | clopf | plopf | ptdf | btheta
case | 0 | 0 | 0 | 0 | 0 | 0 | 0
case3_lmbd | 1 | 0.13874 | 0.224 | 0.38473 | 0.86057 | 0.043997 | 0.046588
case5_pjm | 1 | 0.15282 | 0.15385 | 0.94222 | 1.0716 | 0.018198 | 0.029928
case14_ieee | 1 | 0.12214 | 0.64703 | 0.1156 | 0.083514 | 0.014707 | 0.027705
case24_ieee_rts | 1 | 0.22595 | 0.57633 | 0.10806 | 0.070591 | 0.018364 | 0.024438
case30_as | 1 | 0.18465 | 0.34618 | 0.12371 | 0.28957 | 0.016019 | 0.039052
case30_fsr | 1 | 0.25692 | 1.2546 | 0.61844 | 0.28535 | 0.021648 | 0.062117
case30_ieee | 1 | 0.064638 | 0.28781 | 0.3061 | 0.36278 | 0.010255 | 0.016901
case39_epri | 1 | 0.20495 | 0.24507 | 0.062609 | 0.33094 | 0.0080672 | 0.011757
case57_ieee | 1 | 0.12474 | 0.35047 | 0.19882 | 0.064934 | 0.01001 | 0.025071
case73_ieee_rts | 1 | 0.98689 | 0.24634 | 0.43955 | 0.10234 | 0.11997 | 0.026259
case89_pegase | 1 | 0.82255 | 1.2172 | 1.2734 | 0.057784 | 0.040559 | 0.19123
*Infeasible
Numerical (?) difficulties in specific cases
PRELIMINARY RESULTS

## Slide 24: Conclusions
Benefits of AC-linearized optimal power flow models
  vs DC OPF: power flow accuracy
  vs AC OPF: computational speed
  Based on use of state estimator data in real-world applications
Simplifications required for good “PTDF” implementations
  Active set algorithms
  Line loss relaxation (system/residual losses)
  Factor truncation
  Not trivial… Lots of trial and error
Future work:
  Preprocessing memory & speed improvements
  More intelligent active set implementation
  Computational performance in unit commitment models

## Slide 25: Questions