## Slide 1: A novel optimization approach for sub-hourly unit commitment with large numbers of generators and virtuals
Jianghua Wu1, Bing Yan1, Mikhail Bragin1,
Yonghong Chen2, Peter B. Luh1
1Electrical & Computer Engineering, University of Connecticut
2Midcontinent Independent System Operator (MISO)

## Slide 2: Sub-hourly UC and virtuals
Hourly unit commitment is becoming insufficient for operators to manage power systems efficiently [1]
Sub-hourly UC is a way to improve the reliability of power systems. Comparing to hourly UC,
  Increased number of periods  larger size
  Reduced unit ramping capabilities per period → more active ramping constraints  increased complexity
For certain systems, e.g., MISO’s, there are many virtuals:
  Related to continuous variables only and with linear costs
  Coupled with transmission constraints → dense constraint matrices  increased computation
[1] “FERC Order 764,” Available: https://www.ferc.gov/whats-new/comm-meet/2012/062112/E-3.pdf

## Slide 3: Problem formulation
Sub-hourly UC: the same formulation as hourly UC
Subject to standard
  unit-level constraints, e.g., minimum up/down time, ramp rate and so on
  system-wide constraints, e.g., demand, reserve and transmission capacity
Generation cost, no-load cost and start-up cost
Cost of virtuals
Other costs, e.g., reserve cost

## Slide 4
Consider a MISO’s problem with 1,100 generators and 15,000 virtuals over 36 hours with 15 minutes time intervals
State-of-art branch-and-cut (B&C) does not find a quality solution within 50 minutes because of the difficulties mentioned previously
Our novel decomposition and coordination approach finds a near-optimal solution in 20 minutes
Chart: Feasible solutions over time
First feasible solution by B&C
First feasible solution by our approach
20 min
30 min
Gap:
0.84%
0.9%

## Slide 5: Overview of the presentation
A novel decomposition and coordination approach
  Without formally pursuing optimality for subproblems
Virtuals included in each subproblem
Parallelization
Numerical testing results
Conclusion

## Slide 6
Lagrangian Relaxation (LR)
  A price-based “dual” approach → decompose into subproblems
   reduce complexity exponentially
  Major difficulties:
    Solve all subproblems  time-consuming
    Suffer from major zigzagging of multipliers
    Need to guess the optimal dual value q*
Surrogate LR (SLR): Overcame all above difficulties
  Surrogate optimality condition  guarantee convergence
    Satisfied after solving one subproblem to update multipliers
    Obtain smoother directions with much less effort
  Stepsizing rule without requiring q*
Surrogate Absolute-Value Lagrangian Relaxation (SAVLR)
  Accelerate convergence by adding absolute value penalties
 Death to LR?!

## Slide 7
In our approach, subproblems are formed by
  Dividing generators into subproblems by areas
  Including all virtuals in each subproblem (discuss later)
The objective function of subproblem j at iteration k :
  For each iteration, the simple surrogate optimality condition is checked to guarantee algorithm convergence
  Subproblems are normally solved by B&C in SAVLR
Demand constraints relaxed by multipliers
Absolute value penalties for demand constraints violations
Surrogate dual value

## Slide 8
However, SAVLR may still require a long CPU time
  Long subproblem solving time (≈160s)
Can this be improved? Yes. How?
  A specific property of SAVLR:
    Subproblem solutions only need to be “good enough” to satisfy the surrogate optimality condition
   A new optimization approach inspired by the ordinal optimization concept
    The order is easier to evaluate than the value
    A problem is easier to solve by softening the goal from finding the “best” to finding a “good enough” solution

## Slide 9: A new optimization approach!
Obtain subproblems’ “good enough” solutions without formally pursuing optimality
  Solve simplified models or modify previous solutions  solution candidates  obtain subproblem solutions quickly by “ordering” candidates based on surrogate dual values
  Use B&C to solve subproblems when a good enough solution cannot be obtained (rarely)
  Reduce the subproblem solving time significantly (160s → 50s)
When the surrogate optimality condition is satisfied:
  Even though the quality of subproblem solutions may not be as good as those obtained by B&C, the overall solution quality is not affected
  The total number of iterations needed is about the same as that in SAVLR+B&C

## Slide 10: Flow chart
Subproblems are generally solved by ordering solution candidates
Reduce the solving time significantly
Can this be further improved? How?
Go to next subproblem
Search for better feasible solution by adjusting latest results
Surrogate optimality condition satisfied?
Update multipliers and penalty coefficients
No
Yes
Solve a subproblem by ordering solution candidates. If not solved, use B&C
Initialized by simplified model
Stopping criteria satisfied?
Yes
No

## Slide 11: Virtuals included in each subproblem
To obtain fast convergence, virtuals are not divided into subproblems
Divide virtuals into subproblems → results change dramatically across iterations → slow convergence
Include virtuals in each subproblem → fast convergence
Chart: Surrogate dual values over iterations
virtuals may deviate drastically across iterations
Multiplier values change significantly
virtuals are related to continuous variables only and with linear costs
virtuals and multipliers are very sensitive to each other

## Slide 12: Parallelization
Parallelization is used to further accelerate the approach
  However, there are some difficulties
    Solving all subproblems in parallel  multipliers suffer from major zigzagging as observed in traditional LR
    Having different values for virtuals in different subproblems
    Merging subproblem results may violate the convergence condition even though each of them meets the convergence condition
  To overcome these difficulties,
    Solving a subset of subproblems at a time
    Using the combination of subproblem solutions that meet the surrogate optimality condition
    Fixing generators’ variables based on the merged results, and solving an additional subproblem to obtain the values for virtuals

## Slide 13: Flow chart of the parallel version
Stopping criteria satisfied?
Go to next set of SPs
SP: subproblem
No
Initialized by a simplified model
Yes
Search for better feasible solution by adjusting latest results
No
Solve SP2
Solve SP3
Solve SP1
Combine results of m SPs
Any combination satisfy convergence condition?
m=3
m=m-1
If m=1?
Yes
Solve virtual subproblem
Update multipliers and penalty coefficients
Choose the best subproblem
No
Yes
Solve a few subproblems in parallel. If not solved, use B&C
Build …
Build model1
Build model2
Build subproblem models in parallel  much reduce CPU time

## Slide 14
Testing on multiple MISO’s UC problems, which are hard even for hourly UC (> 20 min)
  With about 1,100 generators and 15,000 virtuals
  Over 36 hours with 15 minute time intervals
Implementation
  Python 2.7 and Gurobi 7.5.0
  HP EliteBook with MISO’s server, Intel® Core (TM) i7-7600U CPU @ 2.80 GHz RAM 16 GB
To measure solution quality, the best known lower bounds are obtained by B&C in advance
Numerical testing results

## Slide 15
Case 1: 1105 generators; 15843 virtuals; 227 transmission lines |  |  |  | 
 | Solving Time (s) | Total Time (s) | Iteration # | Gap (%)
B&C | 5211 | 5443 | N/A | 0.9
SAVLR+B&C | 2985 | 4086 | 20 | 0.9
SAVLR+OO +B&C (sequential) | 1484 | 3237 | 20 | 0.77
SAVLR+OO +B&C (parallel) | 979 | 1639 | 20 | 0.84
Our approach never uses B&C to obtain the subproblem solution in this case
Our approach uses the same number of iterations to obtain the feasible solution and reduces the subproblem solving time from 162s to 53s
Our approach outperforms pure B&C and SAVLR+B&C
Chart: Feasible solutions over time
20 min
30 min
Gap:
0.84%
0.9%
0.9%
0.77%

## Slide 16
Case 2: 1109 generators; 16504 virtuals; 220 transmission lines |  |  | 
 | Solving Time (s) | Total Time (s) | Gap (%)
B&C | 2548 | 3000 | 2
Our approach (parallel) | 990 | 1409 | 1.1
Case 3: 1118 generators; 14955 virtuals; 226 transmission lines |  |  | 
 | Solving Time (s) | Total Time (s) | Gap (%)
B&C | 2787 | 3120 | 4.31
Our approach (parallel) | 638 | 993 | 3.09
Case 4: 1102 generators; 14482 virtuals; 235 transmission lines |  |  | 
 | Solving Time (s) | Total Time (s) | Gap (%)
B&C | 3089 | 3600 | 76
Our approach (parallel) | 619 | 1016 | 1.6
The parallel version of our approach obtains near-optimal solutions efficiently in multiple hard cases, and the results demonstrate that the approach is robust

## Slide 17: Conclusion
SAVLR+OO+B&C is a vast improvement over traditional LR
  New optimization concept!
    Without formally pursuing optimality of subproblems  drastically reduces subproblems’ solving time
  Virtuals included in each subproblem  fast convergence
  Efficient parallelization  with further speedup
Exciting results
  Our approach takes the same number of iterations as those of SAVLR to obtain feasible solutions of the same quality but with much reduced subproblem solving time
  Our approach obtains near-optimal solutions within 20 minutes while B&C could not find a quality solution within 50 minutes
The approach has potential to solve other complex problems in power systems and beyond

## Slide 18
Thank you!