## Slide 1: Optimality Conditions and Cost Recovery in Electricity Markets with Variable Renewable Energy and Energy Storage
FERC Technical Conference, June 24 2020
Prof. Magnus Korpås
Dept. of Electric Power Engineering
NTNU
magnusk@ntnu.no
Dr. Audun Botterud
Lab for Information and Decision Systems, MIT
Energy Systems Division, Argonne National Lab
audunb@mit.edu

## Slide 2
Common hypothesis:
Traditional electricity markets fail under large-scale penetration of wind and solar
  Wind and solar have zero marginal cost
Prices collapse and costs are not recovered in the long run
Our main result:
All plants recover their costs in (perfect) energy-only markets with wind and solar
  Holds true with and without energy storage
Think twice before embarking on complete re-design of electricity markets

## Slide 3: Prediction of Future Price Impacts of VRE
Projected generation portfolios usually not in economic equilibrium!
Mills et al. , 2020

## Slide 4: Investments in Variable Renewables and Storage
Investments in variable renewable energy (VRE) and energy storage (ES) have been driven, in part, by incentive schemes
  Feed-in tariffs/premiums, auction schemes, carbon pricing, net metering (Europe)
  Production and investment tax credits, renewable portfolio standards, net metering, energy storage mandates (United States)
Rapid reduction in costs for VRE and ES
How do these technologies influence thermal generation investments and market equilibrium in a competitive market?
  Schmalensee, MIT (2019), Joskow, MIT (2019)

## Slide 5: System Optimality and Market Equilibrium
Most electricity markets are based on marginal cost pricing
Gives the optimal solution for the system in theory
  System demand is met at minimum costs
  All GenCos (price-takers) maximize their profits and recover their costs (Green 2000, Stoft 2002)
We assume energy-only markets
  Scarcity pricing ensure cost recovery of peaker (and all other) plants
  No explicit capacity remuneration mechanism considered
    They do influence market outcomes and prices (Kwon et al. 2019)
  No direct incentive schemes for VRE and ES
    Competing on equal terms with other technologies

## Slide 6: System Cost Minimization Problem
Sets:
Energy
storage
Generation and demand: q
Capacity: x
Fixed cost: F
Variable cost: v
Availability factor: AF
Peaker
Base
VRE
Demand
Load shedding
Total cost
Load balance
Capacity
constraints
Storage conservation

## Slide 7: Profit Maximization for Technology i
Energy
storage
Peaker
Base
VRE
Demand
Load shedding
Generation and demand: q
Capacity: x
Fixed cost: F
Variable cost: v
Electricity price: p
Annual Revenue: AR
Annual Cost: AC

## Slide 8: Market Equilibrium with Thermal Generation
System optimality conditions gives optimal durations of all generators
Profit maximization gives the same result
Cost recovery is ensured in optimum
- duration of load shedding
- duration of peaker operation
Load duration curve approach
  Green (2000), Stoft (2002)
  Inelastic demand
  No chronological effects
  No operating reserves

## Slide 9: System Optimality Conditions
Peaker plant
Baseload plant
- duration of load shedding
- duration of peaker operation
Load duration curve

## Slide 10: Profit Maximization for Peaking Unit
Same optimality condition as for system.
Cost recovery:
The same holds true for the base plant.

## Slide 11: Market Equilibrium with VRE
and are independent of VRE level
  Cost recovery for peak and base plants
Base duration, , must be determined
  Cost recovery for VRE plant
Introduction of VRE () tends to give
  Less baseplant capacity and energy
  Slightly more peaker capacity
  Slightly more load shedding
  Some VRE curtailment
Net load duration curve approach
  e.g. Kennedy (2005)
  Net demand:
  Linear VRE scaling:

## Slide 12: Optimality Conditions with VRE
System optimality condition for the VRE plant given:
tb gives the optimal VRE capacity from net demand duration curve
Profit maximization gives same optimality conditions:
Cost recovery of VRE plant also ensured,

## Slide 13: Market Equilibrium with Energy Storage
ES is challenging to include in duration curve modelling due to the energy storage level constraint
  We can model power capacity limitation and efficiency explicitly, but not the energy storage constraint
  Previous examples include Steffen and Weber (2013)
We have derived optimality conditions for different EES operating assumptions
  ES charging with «surplus» VRE energy only
    Limited storage: Discharing only replaces base generation
    Unlimited storage: Discharing at any time
  General model with ES for price arbitrage across time periods

## Slide 14: ES for Surplus VRE: Limited Storage
Optimality condition for ES determines the duration of maximum charging
  : Price set by most expensive generator in operation.
  : Price set by the storage opportunity cost. It is the value of one more kWh stored energy.
  : Price set by VRE.
Introduction of EES increases the dispatch of VRE
No change in thermal capacity, but less base dispatch
Optimality conditions for ES:

## Slide 15: ES for Surplus VRE: Unlimited Storage
Optimality conditions for ES:
Optimality conditions for VRE also changes
  Lower base duration, tb
Introduction of ES increase VRE capacity, reduces thermal capacity

## Slide 16: ES for General Price Arbitrage
Indirect representation of storage limitation
  ES stores VRE -> Replace Base
  ES stores Base -> Replace Peak+Shedding
Optimality condition for ES determines the duration of maximum charging and the duration of peaker
  4 non-linear equations with four unknowns

## Slide 17: Insights from Analytical Model
Profit maximization give same optimality conditions as system cost minimization
  All plants recover their costs in system optimum
Optimal VRE capacity always lead to some «excess» energy due to linear scaling
  Exception: Optimal VRE capacity is zero
Introducing unlimited ES for used for «excess» VRE energy triggers more installed VRE capacity in market equilibrium
VRE and ES reduce average energy prices in equilibrium

## Slide 18: Numerical Example
European aggregated hourly time series for 1 year
  Wind and solar
  Load scaled to 100MW
Costs based on EU Commission reference Scenario 2050
  Technology cost and plant data
  Fuel and carbon prices
Duration curve model based on optimality conditions for all plants
YACEMOD* - LP with chronologial time series is used for validation
*Yet Another Capacity Expansion MODel
Key assumptions
  Peaker p: OCGT
  Baseplant b: CCGT
  VRE plant v: Offshore wind or solar PV
  Energy Storage e: Li-Ion or Pumped hydro
  Price during load shedding: 3000 $/MWh
Three main cases
  Case 1 - Base: Only peaker and baseplant
  Case 2 - Add VRE
  Case 3 - Add VRE and ES

## Slide 19: Load and Net Load Duration Curves

## Slide 20: Installed Wind Capacity as a Function of Investment Cost

## Slide 21: Saturation of Wind Penetration without ES

## Slide 22: VRE Impacts on Electricity Costs
Average Electricity Costs (ACE) decreases as wind and solar becomes more competitive.

## Slide 23: Adding Energy Storage

## Slide 24: ES increases VRE; limited Cost Reduction

## Slide 25: Summary of Results: Capacities and Prices
 | 1 - Base | 2 - VRE | 3 - VRE + ES
Weighted avg. price | 114.9 | 81.6 | 81.4
All technologies break even in all cases
- VRE gives less base, more peak plants
- ES gives more VRE, less base and peak
- VRE and ES give much lower emissions

## Slide 26: Conclusions
All plants recover their costs in a perfect market with VRE and EES
  Gives optimal generation mix to minimize system cost
  The result is identical to profit mazimization of price-taker firms
  Analytical and numerical analyses indicate that thermal generators, VRE, and ES can co-exist in regular energy-only markets
The merit-order effect of VRE changes the capacity mix so that all (remaining) generators recovers their costs
  Just as when new, cheaper thermal generators enters the marked
EES triggers more VRE capacity in equilibrium,
  EES creates a new price segment based on the marginal value of storage, where the VRE gains additional profits.
Theoretical model results are confirmed by standard generation expansion model (LP) with chronological time series inputs

## Slide 27: References
Korpås M, Botterud A., “Optimality Conditions and Cost Recovery in Electricity Markets with Variable Renewable Energy and Energy Storage,” MIT CEEPR, working paper 2020-005.
Schmalensee R., “On the Efficiency of Competitive Energy Storage,” Working Paper, June 16, 2019.
Joskow P L, “Challenges for wholesale electricity markets with intermittent renewable generation at scale: the US experience”, Oxford Review of Economic Policy, Volume 35, Number 2, 2019, pp. 291–331
Botterud A., Auer H., “Resource Adequacy with Increasing Shares of Wind and Solar Power: A Comparison of European and U.S. Electricity Market Designs,” Economics of Energy and Environmental Policy, 9(2), 2020
Kwon J., Zhou Z., Levin T., Botterud A., “Resource Adequacy in Electricity Markets with Renewable Energy,” IEEE Trans Power Systems, Vol. 35, No.1, pp. 773-781, 2020.
Mills A.D., Levin T., Wiser R., Seel J., Botterud A., “Impacts of variable renewable energy on wholesale markets and generating assets in the United States: A review of expectations and evidence,” Renewable and Sustainable Energy Reviews, 120 (109670), 2020.
Askeland M, Jaehnert S, Korpås M (2019), Equilibrium assessment of storage technologies in a power market with capacity remuneration”, Sustainable Energy Technologies and Assessments, Volume 31, February 2019, Pages 228-235
Welisch M., A. Ortner, G. Resch (2016). ”Assessment of RES Technology Market Values and the Merit Order Effect – an Econometric Multi Country Analysis.” Energy & Environment 27(1):105–21.
Praktiknjo A., Erdmann G., “Renewable Electricity and Backup Capacities: An (Un-) Resolvable Problem?” The Energy Journal 37(2): 89-106, 2016.
Stoft S., Power Systems Economics: Designing Markets for Electricity, IEEE Press, 2002.
Steffen B., Weber C., “Efficient storage capacity in power systems with thermal and renewable generation”, Energy Economics, vol. 36, pp. 556-567, 2013
Green R., “Competition in Generation: The Economic Foundations,” Proceedings of the IEEE, vol. 88, no. 2, pp. 128-139, 2000.
Kennedy S., “Wind power planning: assessing long-term costs and benefits,” Energy Policy, Vol. 33, pp. 1661-1675, 2005.

## Slide 28: Optimality Conditions and Cost Recovery in Electricity Markets with Variable Renewable Energy and Energy Storage
FERC Technical Conference, June 24 2020
Prof. Magnus Korpås
Dept. of Electric Power Engineering
NTNU
magnusk@ntnu.no
Dr. Audun Botterud
Lab for Information and Decision Systems, MIT
Energy Systems Division, Argonne National Lab
audunb@mit.edu