## Slide 1: A UNIFIED APPROACH TO SOLVE CONVEX HULL PRICING AND AVERAGE INCREMENTAL COST PRICING FERC Technical Conference on Increasing Real-Time and Day-Ahead Market Efficiency through Improved Software June 23-25, 2020
Yonghong Chen, Consulting Advisor, R&D, MISO
Richard O’Neill, ARPA-E, US Department of Energy (Washington, DC)
The views expressed are not necessarily those of the ARPA-E or the Department of Energy

## Slide 2: Non-convexity creates challenges for pricing
100
0
4h
≥5h
0
Pmin=30
MW
Scheduling (difficult)
  Security constrained unit commitment
Pricing (difficult)
  How to allocate fixed cost to the right time intervals and average over the right MW ranges
Ideal
Reality
Can start up or shut down any time when needed
Requires startup and notification times and has minimum run / down times
Can be dispatched within the capacity with only
Variable cost ($/MWh)
Has minimum MW and
ramp rate limits
Variable cost and
Fixed cost: startup cost ($/start), no load cost ($/h)
Scheduling
  Merit order based on variable cost
Pricing uses Locational Marginal Price (LMP)
  Marginal variable cost to serve last MW
t
t
Pmax=100
MW
t

## Slide 3: Market clearing and pricing models
Unit commitment and economic dispatch (UCED) model for market clearing:
  Optimal solution: ()
Market clearing price (LMP and MCP)
  Fixing commit variables and solve LP
  Locational marginal price, , is calculated from the dual variables
(1)
=d (2)
(3)

## Slide 4: Make-whole payment
LMP only reflects the marginal cost. It may not be able to cover the total avoidable cost under the UCED solution.
Define the profit under commitment block as:
Make-whole payment (MWP) is used to compensate for profit loss and is defined as:
All ISO/RTOs compensate for MWP
  However, MWP is not transparent
4

## Slide 5: Out-of-money generators and uplift
Profit for a generator under and commitment / dispatch signal
Given price , generator owners may solve profit maximizing problem
A generator is “out-of-money” if uplift
Uplift includes MWP and Lost Opportunity Cost (LOC)
  MWP: when resource can make more profit by generating less MW than RTO’s instruction.
  LOC: when resource may make more profit by generating more MW than RTO’s instruction
Non-convexity or sub-optimal commitment
5

## Slide 6: Convex Hull Pricing (CHP) Pricing[1]
CHP pricing is proposed in non-convex market to minimize total uplift and to better support the market clearing solution. CHP incorporates both the marginal costs and the avoidable fixed operating costs of available resources in the market.
CHP price can be solved through the Lagrangian dual problem. However, it’s difficult to converge. Recent advance on UCED resource formulation allows it to be solved with LP relaxation of the UCED problem.
It considers the total available capacity of the online and offline resources and balances the incentives to follow RTOs’ instructions for all resources. It may still require MWP and/or LOC under CHP.
Current implementations are mostly single interval approximation for fast start resources
[1] P. Gribik, W. Hogan, and S. Pope, “Market-clearing electricity prices and energy uplift,” Harvard Univ., Cambridge, MA, working paper, 2007.
6

## Slide 7: CHP and Lagranian Dual Problem[1]
Profit maximization of individual resources
The Lagrangian dual function after dualizing power balance equation is
} +
The Lagrangian dual problem is to find the dual maximizer price. for
Under any price , the gap between the UCED problem and its dual is exactly the total uplift.
  =
The solution of the Lagrangian dual problem can minimize the uplift and is the convex hull price.
is very difficult to converge.
[1] P. Gribik, W. Hogan, and S. Pope, “Market-clearing electricity prices and energy uplift,” Harvard Univ., Cambridge, MA, working paper, 2007.
7

## Slide 8: Solve CHP with LP Relaxation (LIP) of UCED[2][3]
CHP problem MIP:
UCED LP relaxation (LIP):
0
Convex hull
Convex envelope
Under the convex hull and convex envelope formulation: CHP can be solved with LP relaxation (LIP) of UCED[2]
An extended integral UC formulation is developed and an iterative algorithms is developed in [3] to solve CHP with multiple LIPs.
[2] B. Hua and R. Baldick, “A convex primal formulation for convex hull pricing,” IEEE Transactions on Power Systems, 2017
[3] Y. Yu, Y. Guan, Y. Chen, “An Extended Integral Unit Commitment Formulation and An Iterative Algorithm for Convex Hull Pricing”, IEEE Transactions on Power Systems, 2020
8

## Slide 9: Average Incremental Cost (AIC) Pricing[4][5]
AIC pricing is proposed in non-convex market as the rough equivalent to marginal cost pricing in convex markets. It may serve as an entry signal in addition to the LMP.
Similar to CHP, the AIC pricing mechanism produces prices that incorporate both the marginal costs and the avoidable fixed operating costs of a dispatched resource.
AIC pricing focuses on the dispatched MW of online resources and eliminates MWP.
AIC pricing can be solved similar to CHP – By adjusting resource upper bounds based on the UCED solution, the LP relaxation of the UCED problem can also be used to solve AIC prices.
[4] R. P. O’Neill, A. Castillo, B. Eldridge and R. B. Hytowitz, "Dual Pricing Algorithm in ISO Markets," IEEE Transactions on Power Systems, 2017.
[5] Richard O’Neill, Notes on AIC pricing, 2019
9

## Slide 10: Solve AIC with LP Relaxation (LIP) of UCED[6]
AIC can also be solved with LP Relaxation
1. Define set for commitment blocks requiring MWP under LMP:
1. Define set 𝑆^𝑀𝑊𝑃for commitment blocks requiring MWP under LMP:
2. Define p-cut: cut off uncommitted and un-dispatched regions
,
𝑋_(𝑝_(𝑔,𝜀)^∗)^𝐴𝐼𝐶={〖(𝑝〗_𝑔,𝑢_𝑔)∈Χ_𝑔,𝑝_𝑔𝑡≤ 𝑝_𝑔𝑡^(𝐴𝐼𝐶−𝑚𝑎𝑥)), ∀𝑔∈𝐺, 𝑡∈𝑇},
{█(〖min(𝑝〗_𝑔𝑡^∗+𝜀, 𝑝_𝑔𝑡^𝑚𝑎𝑥) 𝑖𝑓 (𝑔,𝑡)∈𝑆^𝑀𝑊𝑃@0 𝑖𝑓 𝑝_𝑔𝑡^∗=0@〖 𝑝〗_𝑔𝑡^𝑚𝑎𝑥 𝑖𝑓 𝑝_𝑔𝑡^∗>0, 𝑎𝑛𝑑 (𝑔,𝑡)∉𝑆^𝑀𝑊𝑃 )┤
}
𝑆^𝑀𝑊𝑃={(𝑔,𝑡)┤| 𝑝_𝑔𝑡^∗>0, 𝑡∈𝐵_(𝑔,𝑗), 𝜑_(〖𝑔,𝐵〗_(𝑔,𝑗) ) (𝐿𝑀𝑃,𝑝_𝑔^∗,𝑢_𝑔^∗ )<0}
where
where 𝑝_𝑔𝑡^(𝐴𝐼𝐶−𝑚𝑎𝑥)=
By adding p-cut based on optimal UCED solution (), under the convex hull and convex envelope formulation.
By adding p-cut based on optimal UCED solution (𝑝_𝑔^∗,𝑢_𝑔^∗), 𝑔∈𝐺 under the convex hull and convex envelope formulation.
AIC can also be solved with LP Relaxation
2. Define p-cut: cut off uncommitted and un-dispatched regions
[6] Y. Chen, R. P. O’Neill, P. Whitman, “A Unified Approach to Solve Convex Hull Pricing and Average Incremental Cost Pricing with Large System Study”, IEEE Transactions on Power Systems, Under Review
10

## Slide 11
AIC problem MIP
UCED LP relaxation (LIP)
0
is a sub-region of with added p-cuts based on
Convex hull
Convex envelope
Under the convex hull and convex envelope formulation, AIC can be solved with LP relaxation of UCED within a sub-region defined based on UCED solution
Unified approach to solve CHP and AIC
UCED MIP with AIC p-cut:
=d
,
11

## Slide 12: AIC price solved from LP relaxation with p-cut can eliminate make whole payments
Proposition 2: Under optimal solution , , For the commitment block requiring MWP under LMP, i.e., the subset , the solution in cannot be .
Proposition 3: Under pricing solution from , the commitment block under subset has $0 MWP when .
AIC can be solved with LP relaxation under the following conditions:
Add p-cut based on the optimal UCED solution
Apply the extended individual resource convex hull & convex envelope formulation in UCED
12

## Slide 13: 2-Generator Example
Using the 3-binary formulation and solving AIC with LP relaxation with p-cut, the price can eliminate MWP but, it is higher than necessary and not a good entry signal.
 |  |  | Cost |  |  | Ramp Rate |  | 
 | Pmin | Pmax | $/MWh | Startup | NoLoad | Normal | Startup | Shut down
Gen1 | 0 | 100 | 10 | 0 | 0 | 100 | 100 | 100
Gen2 | 20 | 35 | 50 | 1000 | 30 | 5 | 22.5 | 35
u,v,e: commitment, startup, shutdown variables
p: dispatch variable
13
t | 1 | 2 | 3 | 
LD | 95 | 100 | 130 | 
AIC2 | 10 | 10 | 1,161 | sum
Gen2 Profit | -$1,830 | -$1,030 | $33,305 | $30,445
Total Profit | $145,563 | Max profit |  | $148,141
Uplift | $2,578 | MWP |  | $0
t | 1 | 2 | 3 | 
LD | 95 | 100 | 130 | 
LMP | 10 | 10 | 90 | 
p2 | 20 | 25 | 30 | sum
Gen2 Profit | -$1,830 | -$1,030 | $1,170 | -$1,690
Total profit | $6,310 | Max profit |  | $8,000
Uplift | $1,690 | MWP |  | $1,690

## Slide 14
t | 1 | 2 | 3 | 
LD | 95 | 100 | 130 | 
AIC | 10 | 10 | 146.33 | sum
Gen2 Profit | -$1,830 | -$1,030 | $2,860 | -$0.10
Total Profit | $13,633 | Max profit |  | $14,770
Uplift | $1,138 | MWP |  | $0.10
Extended generator CHP / convex envelope formulation
Using extended generator convex hull / convex envelope formulation and solving AIC with LP relaxation with p-cut: The price is just enough to eliminate MWP and a good entry signal.
stay off through t and start up at the beginning of t+1, for t=0,1,2
start up at the beginning of t+1 and stay on until the end, for t=0,1,2.
: start up at the beginning of t+1 and shut down at the beginning of k, for .
: shut down at the beginning of t and stay off until the beginning of k+1, for .
14

## Slide 15: CHP and AIC prototype study on MISO size cases
CHP and AIC are prototyped to study revised MISO DA cases including
Energy only with Transmission constraints
Most of generation constraints (limit, ramping, min run / min down / max run times)
Generation costs: hot / intermediate / cold startup times and costs, no load cost and piece wise linear incremental energy cost
Three versions of AIC:
“AIC”: with p-cut and extended generator convex hull / convex envelope formulation
“AIC2”: with p-cut and 3-binary formulation
“AIC34”: with additional p-cut, binary cuts, flow cuts and 3-binary formulation[7]
Binary cuts:
Binary cuts: 𝑢≤𝑢^∗,𝑣≤𝑣^∗,e≤𝑒^∗
CHP and AIC are prototyped to study revised MISO DA cases including
Energy only with Transmission constraints
Most of generation constraints (limit, ramping, min run / min down / max run times)
Generation costs: hot / intermediate / cold startup times and costs, no load cost and piece wise linear incremental energy cost
Three versions of AIC:
*Intel Haswell processor @ 2.5 GHz, 512GB RAM, 32 sockets per CPU, 1 core per socket, 1 thread per core
[7] R. P. O’Neill, Y. Chen, “The One-Pass AIC Approach with Multi-Step Marginal Costs, Ramp Constraints and Reserves”, Working Paper, 2020.
15

## Slide 16: CHP and AIC prototype study on MISO DA case (cont.)
MWP, uplift and profit
CHP: Minimum uplift
AIC: zero or close to zero MWP
Small residuals on AIC and AIC2 are due to small MIP gap in UCED solution
AIC34 can eliminate MWP under sub-optimal UCED solution by adding additional p-cuts, binary cuts and flow cuts [7].
Transmission constraints not binding in UCED may bind in CHP and/or AIC runs, resulting in FTR uplift
16

## Slide 17: Application of the advanced pricing methods
17
Remaining technical issues to be addressed before CHP or AIC can be used as market clearing prices
  Real time rolling market clearing window issue is not fully addressed: commitment costs prior to the clearing window become sunk costs
  Emerging non-traditional resources: on-going research to derive extended convex hull & convex envelope formulation for multi-configuration combined cycle, storage, etc.
Potential near term application: estimate the total operational cost for reserve and regional transfer constraints
Under uncertainty, operations may take emergency actions for system-wide or regional reliability
Shadow prices from current operating reserve and regional transfer constraints may not fully reflect the cost of those actions
MISO single interval approximate ELMP may help to reflect fast-start resource commitment cost
AIC and CHP prices from multi-interval UCED can better reflect full costs from commitment and emergency actions
Potentially help on defining reserve demand curves (e.g., ORDC) and regional transfer demand curves

## Slide 18: References
[1] P. Gribik, W. Hogan, and S. Pope, “Market-clearing electricity prices and energy uplift,” Harvard Univ., Cambridge, MA, USA, working paper, 2007.
[2] B. Hua and R. Baldick, “A convex primal formulation for convex hull pricing,” IEEE Transactions on Power Systems, vol. 32, no. 5, pp. 3814–3823, 2017
[3] Y. Yu, Y. Guan, Y. Chen, “An Extended Integral Unit Commitment Formulation and An Iterative Algorithm for Convex Hull Pricing”, IEEE Transactions on Power Systems, Accepted, 2020
[4] R. P. O’Neill, A. Castillo, B. Eldridge and R. B. Hytowitz, "Dual Pricing Algorithm in ISO Markets," IEEE Transactions on Power Systems, vol. 32, no. 4, pp. 3301-3310, 2017.
[5] Richard O’Neill, Notes on AIC pricing, 2019
[6] Y. Chen, R. P. O’Neill, P. Whitman, “A Unified Approach to Solve Convex Hull Pricing and Average Incremental Cost Pricing with Large System Study”, IEEE Transactions on Power Systems, Under Review
[7] R. P. O’Neill, Y. Chen, “The One-Pass AIC Approach with Multi-Step Marginal Costs, Ramp Constraints and Reserves”, Working Paper, April, 2020.
18