## Slide 1
Scalable Energy System Expansion Under Uncertainty Using Multi-stage Stochastic
Optimization
Devon Sigler, Jonathan Maack, Ignas Satkauskas, Matthew Reynolds, Wesley Jones

## Slide 2: Overview
Scalable Integrated Infrastructure Planning
Multi-Stage modeling can be done at scale for power system infrastructure expansion problems
Multi-Stage modeling allows for detailed representations of system operations and uncertainty
Progressive Hedging provides a useful tool for solving such models at scale and can be effectively run on HPC systems
Additional stages representing uncertainty do cause different build decisions, and moving forward it might be beneficial to explicitly consider uncertainty in renewables and operations when analyzing expansion decisions

## Slide 3: General Infrastructure Expansion Model
What detail is needed in O(x)?

## Slide 4: Network Complexity

## Slide 5: Scenario Based Optimization Under Uncertainty
Infrastructure planning decisions should be co-optimized against many potential operational scenarios
Allows for planning decisions to be made under uncertainty
Allows for inclusion of important scenarios when it is not obvious which are the important ones
Two Stage Scenario Based Model
Could have a multi-stage representation of operations

## Slide 6: Sparsity Structure
Scalable algorithms exist for solving multi-stage scenario based optimization problems
Progressive Hedging (PySP)
Schur Complement based iterative methods (IPOPT,PIPSNLP)

## Slide 7: Transmission Expansion Problems
Traditional solution approaches are limited in the sources and detail of uncertainty they can consider
  Few operational scenarios are considered
  Renewable generation forecasts are assumed to be perfect
  Time scales tend to be either
    Long
    Snap shots in time
What is lost by ignoring various forms of uncertainty?
Scalable Integrated Infrastructure Planning

## Slide 8: Two Stage vs. Three Stage Models

## Slide 9: Experiment: Effects of Wind Uncertainty
2-Stage
Load and wind uncertainty handled simultaneously
Effectively modeling grid operations only with perfect renewable forecasts
Builds a system that can operate under many different load profiles when there is no uncertainty in the wind
3-Stage
Load and wind uncertainty in different stages
Modeling grid operations with uncertain wind generation
Leads to decisions informed by more cautious operating decisions
Goal: Understand the effects of uncertainty in wind generation on transmission expansion decisions
Load and Wind
Wind
Load

## Slide 10: Progressive Hedging Concept
Horizontal technique for solving multi-stage scenario based stochastic programs
Solves individual subproblems with penalty terms to force consensus over time amongst the first stage decision variables
Converges linearly when subproblems are convex
Rockafellar, R. Tyrrell, and Roger J-B. Wets. "Scenarios and policy aggregation in optimization under uncertainty." Mathematics of operations research 16, no. 1 (1991): 119-147

## Slide 11: Progressive Hedging Implementation
ProgressiveHedging.jl
Implements the progressive hedging algorithm in a meta-solver package for decomposition and parallel solution of structured optimization problems. Jonathan Maack from NREL is the lead developer. Jonathan.Maack@NREL.gov
Implementation of the progressive hedging algorithm in the Julia language
Uses the Julia Distributed.jl package, an implementation of distributed memory parallel computing
User provides a function for constructing a JuMP model for an instance of scenario data
User provides a dictionary of model variables for each stage
User provides a multi-stage scenario tree with probabilities
Rockafellar, R. Tyrrell, and Roger J-B. Wets. "Scenarios and policy aggregation in optimization under uncertainty." Mathematics of operations research 16, no. 1 (1991): 119-147
https://github.com/jump-dev/JuMP.jl
https://github.com/NREL/ProgressiveHedging.jl

## Slide 12: SIIP Framework: An example for electricity systems
Rigorous data model that defines infrastructure systems
Collects information required for device level modeling
Includes parsing capabilities
Exploits Julia’s parametric dispatch for efficient code development
Agnostic to simulations that will be performed
PowerSystems.jl
Mathematical formulations and simulation assemblies
Support for optimization and dynamic simulation models
Modular problem assembly to enable rapid development and extension
Includes standard simulations (e.g. UC/ED)
Deep integration with PowerModels.jl (LANL) to enable non-linear power flow formulations
PowerSimulations.jl
Modular, interoperable, modeling components that define infrastructure modeling problems informed by system data
SIIP::Power

## Slide 13: An Integrated Modeling Vision
Framework Design Objectives
Modularity and Accessibility – flexible and transparent problem creation that is easily extensible
Integration – coherency between models representing distinct phenomena
Scalability – address scales that matter through efficient problem simulation and parallelism
Buildings
Buildings
Buildings
Buildings
Buildings
Buildings
Liquid Fuels
Transportation
Thermal
Electricity
Gas
Water
Liquid Fuels
Transportation
Thermal
Electricity
Gas
Water
Liquid Fuels
Transportation
Thermal
Electricity
Gas
Water
Liquid Fuels
Transportation
Thermal
Electricity
Gas
Water
Distribution - Interconnection
Devices - Distribution
Seconds - Minutes
Minutes - Seasons
Years - Decades
Liquid Fuels
Transportation
Thermal
Electricity
Gas
Water
Steady-State/Dynamics
Scheduling
Investment
Data/Methods
Modeling Tools
Liquid Fuels
Transportation
Thermal
Electricity
Gas
Water

## Slide 14: Leveraging SIIP
Use SIIP framework to read data and build models
  PowerSystems.jl provides needed parsing capabilities
  PowerSimulations.jl provides model building
Alter constructed models to fit our formulation
Reduces debugging time enormously
(https://github.com/NREL/PowerSystems.jl and https://github.com/NREL/PowerSimulations.jl)

## Slide 15: RTS-GMLC
RTS-GMLC is a modernized version of the IEEE Reliability Test System-1996. It was developed to satisfy the need for a standardized data base to test and compare results from different power system reliability evaluation methodologies.
Buses 73
Lines 120
Generators 158
Three weakly connected regions
https://github.com/GridMod/RTS-GMLC

## Slide 16: Problem Setup
RTS-GMLC test system using DCOPF
16 hours used
  4 days, one from each season
  4 times from each day
20 wind scenarios for each hour to total 320 scenarios
Each hour is 12 periods at a 5 minute resolution
Line flow constraints where modified as follows
(https://github.com/GridMod/RTS-GMLC)
Table 1: Variables of Three-Stage Stochastic Program.
Expansion
Decisions
Operations Model
Generator Setpoints
Wind Setpoints,
Slack Variables
1
)
Three-Stage Stochastic Program Formulation.

## Slide 17: Realistic Wind Scenarios
Scenario Selection Process. Blue represents preprocessing while red represents repeated steps for each second stage node. This data driven approach preserves spatiotemporal correlations present in the WTK data.
Wind Power Scenario for Each of the 22 Wind Farms. These are 6 steps at 5-minute resolution. Scenarios are given as deviations from persistence. Significant changes in wind power occur even for a single wind farm over 30 minutes.
https://www.nrel.gov/grid/wind-toolkit.html
Conference paper on these techniques accept at the 2020 IEEE PES General Meeting

## Slide 18: Visualization of Results
The lines that were expanded are all near the large wind resources on the grid. The line that is not still seems to enable a transmission path from a large wind farm.
Map of the RTS-GMLC Network. 73 buses (red dots), 22 wind-generating buses (blue circles), 445 WTK wind sites (heat map), 120 transmission lines (black lines), and 4 expansion decisions (red lines)

## Slide 19: Results
We compared our 3 stage model expansion decisions with a 2 stage model where in the 2 stage a single wind scenario was considered for each of the 16 load cases
Large 3 stage model solved in less than 2 hours
The the same lines were expanded in both cases however in 3 out of 4 lines the 3 stage model chose a larger increase in line capacity

## Slide 20: Strong Scaling
Strong Speed Up of ProgressiveHedging.jl. All runs were conducted on Eagle. IPOPT with HSL linear solver MA57 was used for the PH subproblem solutions.

## Slide 21: Weak Scaling
Weak Scaling of ProgressiveHedging.jl. All runs conducted on Eagle. IPOPT with HSL linear solver MA57 was used to solve the subproblems. Wall clock time gives the average time for a PH iteration. Each core solved four subproblems.

## Slide 22: Sources of Large Power Systems Models
Temporal resolution
  Timescale resolution
  Number of timescales
Spatial resolution
  Number of nodes in the network
  Number of devices on the network
Representation of Stochastic Quantities
  Load, wind, solar, hydro, policy
  Future generation investments
  Optimization Stages
Representation of System Physics
  Transport, DCOPF, ACOPF, dynamics

## Slide 23: Decomposition on the HPC
Using Progressive Hedging problems can be formulated in a decomposed manner
Each scenario is a single JuMP model that can live in memory on its own HPC compute node
Each scenario then can leverage the memory of the node it is on as well as the cores on that node
This allows for huge problems to be stored on the HPC across nodes and for the compute resources of each node to be used on each scenario subproblem.
Allows subproblems to be more detailed in time, space, and physics
Summary: Large problems, lots of detail, using lots of memory across nodes, and lots computational power on each subproblem

## Slide 24: Summary
Multi-Stage modeling can be done at scale for power systems infrastructure expansion problems
Progressive Hedging provides a useful tool for solving such models at scale and can be effectively run on HPC systems
Additional stages representing uncertainty do cause different build decisions, and suggest moving forward it might be beneficial to explicitly consider uncertainty in renewables and operations when making expansion decisions
Using decomposition techniques allows for extremely large problems to be solved and additional detailed to be added into each scenario when using HPC resources
Sigler, Devon, Jonathan Maack, Ignas Satkauskas, Matthew Reynolds, and Wesley Jones. "Scalable Transmission Expansion Under Uncertainty Using Three-stage Stochastic Optimization." In 2020 IEEE Power & Energy Society Innovative Smart Grid Technologies Conference (ISGT), pp. 1-5. IEEE, 2020.

## Slide 25: Questions